## Slide 1
How AI is Advancing Early Pneumonia Detection and Improving Patient Care: Driving Better Patient Outcomes through AI-Based Chest X-Ray Analysis
Denali Carpenter

## Slide 2
Why Pneumonia Matters
Widespread & Serious
Pneumonia is a leading cause of hospitalization and death worldwide, especially among young children and older adults.
Importance of Early Detection
Prompt diagnosis can significantly reduce complications, hospital stays, and overall mortality rates.
Resource Constraints
Many healthcare facilities face a shortage of radiologists, making timely diagnosis challenging.

## Slide 3
How AI Can Help
Faster X-Ray Analysis
AI can quickly flag potential pneumonia cases on chest X-rays, acting as an extra set of expert eyes for busy radiologists.
High Accuracy
Advanced deep learning models have demonstrated results comparable to experienced clinicians and radiologists, ensuring fewer missing cases.
Better Patient Outcomes
Earlier detection means faster treatment and improved recovery, ultimately saving lives and resources.
By harnessing AI for chest X-ray interpretation, healthcare providers can deliver more efficient, accurate, and timely pneumonia diagnoses – improving both patient outcomes and the overall healthcare system.

## Slide 4
Overview
1. Problem Statement
Use machine learning to classify chest x-rays and evaluate efficacy.
2. Data
Chest X-Ray images from academic research were used.
3. Data Exploration
Image differences between pneumonia and healthy were explored.
4. Data Processing
Images were prepped for use in traditional ML and Deep Learning
5. Modeling
Use traditional ML, neural networks, and transfer learning
6. Conclusion
Best model comparable to trained radiologist.
This presentation showcases how advanced machine learning techniques can revolutionize pneumonia detection, leading to better patient outcomes and more efficient treatment strategies.

## Slide 5
1. Problem Statement
Evaluating the Effectiveness of Machine Learning Techniques for Bacterial and Viral Pneumonia Detection in Chest X-Ray Images

## Slide 6
Research Questions
What is the most effective and efficient model for predicting pneumonia diagnoses from chest x-ray images?
Follow Up: Can we accurately distinguish between viral and bacterial pneumonia via chest x-ray images?

## Slide 7
2. Data
Chest X-ray Images

## Slide 8
Raw Chest X-Ray Images

## Slide 9
Data Overview*
Dataset
Training
Testing
Validation
Total Images
5,216
624
16
NORMAL
1,341
234
8
PNEUMONIA
3,875
390
8
*Counts show dataset before cleaning.

## Slide 10
3. Data Exploration
Examining Differences in PNEUMONIA and NORMAL Images

## Slide 11
Data Exploration
Brightness & Contrast Differences
Analyzed X-ray brightness and contrast levels to see how pneumonia images differ from healthy ones.
Texture Patterns in Images
Examined patterns in the images to detect subtle texture differences that might indicate pneumonia
Sharpness and Blurriness
Checked how sharp or blurry different X-rays were, helping identify key differences between normal and pneumonia cases.
Simplifying the Data for AI
Reduced the complexity of image data while keeping important details, making it easier for AI to learn patterns effectively.
The data analysis revealed key differences between normal and pneumonia X-rays, helping to build an AI model that can detect pneumonia more accurately and efficiently.

## Slide 12
Most Images are of Bacterial Pneumonia

## Slide 13
4. Data Processing
Extracting and Adjusting Images to Improve Accuracy

## Slide 14
Data Cleaning
Remove Duplicates
Check for corrupt images
Match formatting (size and color)
Augment images

## Slide 16
5. Modeling
Building and Testing Traditional Machine Learning and Deep Learning Techniques

## Slide 17
Traditional Machine Learning Techniques Used
1
Random Forest Models
(lots of decision trees!)
2
Support Vector Machines
(what if we examined only the most important data points?)
3
Hyperparameter tuning
(adjusting AI model settings for better performance)

## Slide 18
Deep Learning Techniques Used
1
Convolutional Neural Network
(an advanced neural network built for image data)
2
Transfer Learning: VGG16 and DenseNet121
(pretrained AI models designed to recognize patterns in 1000 image categories)
koala
minivan
violin

## Slide 19
koala
minivan
violin
VGG16 or DenseNet121
… 997 other categories
The Idea Behind Transfer Learning

## Slide 20
VGG16 or DenseNet121
Retrain the model to recognize pneumonia instead of objects like animals or cars
pneumonia
healthy/normal
The Idea Behind Transfer Learning
This isn't the full story—but it's enough to understand how AI can quickly get really good at medical image tasks

## Slide 21
Model Evaluation and Comparison: Accuracy
Accuracy = Percentage of Correctly Identified Images
Tuned Random Forest
69%
Ensemble of Random Forests
69%
Tuned SVM
70%
Base SVM
70%
DenseNet121
88%
Custom CNN
88%
VGG16
95%

## Slide 22
Best model: VGG16 with transfer learning applied
94.82%
Accuracy
(Measures the overall percentage of correct predictions, including both pneumonia and healthy cases.)
93.61%
Precision
(Measures how often predicted pneumonia cases are correct.)
98.45%
Recall
(Measures how often the system correctly detects pneumonia when it is present.)
88.74%
Specificity
(Measures how often the system correctly identifies healthy patients.)

## Slide 23
11%
False Positive Rate

## Slide 24
1.6%
False Negative Rate

## Slide 25
6. Conclusion
What Does this Mean and How Does it Help?

## Slide 26
Radiologist and Clinician Performance versus VGG16 Model
Recall (sensitivity) Measures how often the system/individual correctly detects pneumonia when it is present.
Specificity Measures how often the system correctly identifies healthy patients.

## Slide 27
Real-World Impact
The high recall achieved by the deep learning models is critical in a clinical setting, where missing a pneumonia diagnosis could lead to delayed treatment and serious consequences for patients. There is potential for this work to transform healthcare by enabling early and accurate pneumonia detection, which can significantly improve patient outcomes and treatment strategies.

## Slide 28
Conclusion
Demonstrated power of deep learning
Developed highly accurate and reliable diagnostic tool for pneumonia detection using advanced machine learning techniques, particularly deep learning models.
Potential to transform healthcare
Has the potential to significantly improve early detection and treatment of pneumonia in healthcare settings, enabling better patient outcomes and more efficient treatment strategies.
Contribution to 'Uncharted & Unstoppable'
This study showcases how innovative technology can drive meaningful change and push boundaries in healthcare.
This study demonstrates the remarkable potential of deep learning in developing accurate and reliable diagnostic tools for pneumonia detection in chest X-ray images. The researchers' work has the power to revolutionize healthcare by enabling early and precise diagnosis, leading to improved patient outcomes and more efficient treatment strategies.

## Slide 29
Thank you!